WagMan Tests
Git commit: aa17876a17046f7e6f2e37966d05902c7047ae09

Test Group	Test Description	Test Methodology	Pass/Fail
Primary boot sequence	Multiple attempts at primary boot sequence	Disconnect heartbeat from NC until SysMon tries another boot. Reconnect heartbeat and see if everything boots.
	Going to sleep	Disconnect heartbeat from NC and leave it until SysMon goes to sleep.
	All EEPROM defaults set correctly	Go thru list and make sure every variable is being assigned a default.
	Parameters transferred correctly from NC	Print the value of an EEPROM read after receiving the parameters.
	Time transferred correctly from NC	Print the time received from NC.
Boot SysMon	Bad power	Set default EEPROM value to zero.
	Bad environment	Set default EEPROM values to something outside the ambient range.
Boot NC	Bad power	Set default EEPROM value to zero.
	Bad power resulting in permanent disable	With the EEPROM value at zero, let SysMon disable NC. Reboot SysMon and see if it attempts to boot NC.
	Bad environment	Set default EEPROM values to something outside the ambient range.
	Bad temperature	Set default EEPROM values to something outside the ambient range.
	Bad heartbeat	Disconnect heartbeat from NC and wait for power cycle. Reconnect heartbeat and see if it boots correctly.
Boot ethernet switch	Bad power	Set default EEPROM value to zero.
	Bad power resulting in permanent disable	With the EEPROM value at zero, let SysMon disable the switch. Reboot SysMon and see if it attempts to boot the switch.
	Bad temperature	Set default EEPROM values to something outside the ambient range.
Boot guest nodes	Bad power	Set default EEPROM value to zero.
	Bad power resulting in permanent disable	With the EEPROM value at zero, let SysMon disable GN. Reboot SysMon and see if it attempts to boot GN.
	Bad temperature	Set default EEPROM values to something outside the ambient range.
	Bad heartbeat	Disconnect heartbeat from GN and wait for power cycle. Reconnect heartbeat and see if it boots correctly.
Main loop	Serial receive	Print the character that was just received.
	Status report	Verify contents of status report received by NC.
	Time report	Verify contents of time report received by NC.
	Problem report	Verify contents of problem report received by NC. Some of the other tests should cause problem reports to be sent.
	All timeouts being responded to	Cause each timeout by setting values to something ridiculous and overriding boot checks.
	Reboot devices	Cause a timeout for each device and see if it SysMon reboots it after awhile. Also need to make sure normal operation resumes smoothly after the delay of waiting for something to boot.
WagMan on NC	Heartbeat output	Verify heartbeat on the oscilloscope.
	Store status report	Write status report to file.
	Store problem report	Write problem report to file.
	Store time report	Write time report to file.