WagMan Tests

Test Group	Test Description	Test Methodology	Pass/Fail
Primary boot sequence	Multiple attempts at primary boot sequence	Disconnect heartbeat from NC until SysMon tries another boot. Reconnect heartbeat and see if everything boots.	pass
	Going to sleep	Disconnect heartbeat from NC and leave it until SysMon goes to sleep.	fail
	All EEPROM defaults set correctly	Go thru list and make sure every variable is being assigned a default.	pass
	Parameters transferred correctly from NC	Print the value of an EEPROM read after receiving the parameters.	pass
	Time transferred correctly from NC	Print the time received from NC.	pass
Boot SysMon	Bad power	Set default EEPROM value to zero.	pass
	Bad environment	Set default EEPROM values to something outside the ambient range.	pass
Boot NC	Bad power	Set default EEPROM value to zero.	pass
	Bad power resulting in permanent disable	With the EEPROM value at zero, let SysMon disable NC. Reboot SysMon and see if it attempts to boot NC.	pass
	Bad environment	Set default EEPROM values to something outside the ambient range.	pass
	Bad temperature	Set default EEPROM values to something outside the ambient range.	pass
	Bad heartbeat	Disconnect heartbeat from NC and wait for power cycle. Reconnect heartbeat and see if it boots correctly.	pass
Boot ethernet switch	Bad power	Set default EEPROM value to zero.	pass
	Bad power resulting in permanent disable	With the EEPROM value at zero, let SysMon disable the switch. Reboot SysMon and see if it attempts to boot the switch.	pass
	Bad temperature	Set default EEPROM values to something outside the ambient range.	pass
Boot guest nodes (1, 2, 3)	Bad power	Set default EEPROM value to zero.	pass
	Bad power resulting in permanent disable	With the EEPROM value at zero, let SysMon disable GN. Reboot SysMon and see if it attempts to boot GN.	pass
	Bad temperature	Set default EEPROM values to something outside the ambient range.	pass
	Bad heartbeat	Disconnect heartbeat from GN and wait for power cycle. Reconnect heartbeat and see if it boots correctly.	pass
Main loop	Status report	Verify contents of status report received by NC.	pass
	Time report	Verify contents of time report received by NC.	pass
	Problem report	Verify contents of problem report received by NC. Some of the other tests should cause problem reports to be sent.	pass
	All timeouts being responded to	Cause each timeout by setting values to something ridiculous and overriding boot checks.	pass
	Reboot devices	Cause a timeout for each device and see if it SysMon reboots it after awhile. Also need to make sure normal operation resumes smoothly after the delay of waiting for something to boot.	pass
WagMan on NC	Heartbeat output	Verify heartbeat on the oscilloscope.	pass
	Store status report	Write status report to file.	pass
	Store problem report	Write problem report to file.	pass
	Configure (and communicate with SysMon) correctly	Run configure script on NC and see if status messages are eventually being sent to NC.	pass